FREQUENCY-DOMAIN METHODS FOR NONLINEAR ANALYSIS

Theory and Applicalions

by

### G.A. Leonov

## St.Petersburg University, Russia

### D.V. Ponomarenko

## St.Petersburg University, Russia

### V.B.Smirnova

## St.Petersburg University, Russia

World Scientific

Singapore – New Jersey -  London – Hong Kong

Published by

World Scientific Publishing Co Pte Ltd

P O Box 128, Farrer Road, Singapore 912805

USA office: Suite 1B, 1060 Main Street, River Edge, NJ 07661

UK office: 57 Shelton Street, Covent Garden, London WC2H 9HE

British Library Cataloguing-in-Publication Data

A catalogue record for this book is available from the British Library.

FREQUENCY-DOMAIN METHODS FOR NONLINEAR ANALYSIS: THEORY AND APPLICATIONS

Copyright © 1996 by World Scientific Publishing Co. Pte. Ltd.

All rights reserved. This book, or parts thereof, may not be reproduced in any form or by any means, electronic or mechanical, including photocopying, recording or any information storage and retrieval system now known or to be invented, without written permission from the Publisher.

For photocopying of material in this volume, please pay a copying fee through the Copyright Clearance Center, Inc., 222 Rosewood Drive, Danvers, MA 01923, USA.

ISBN 981-02-2146-0

This book is printed on acid-free paper. Printed in Singapore by Uto-Print

Preface

Main way of the development of the theory of the dynamical systems in the twentieth century is the investigation of attractors. In the first three decades of the present century the attention of the researchers was concentrated on the attractors consisting of the single stationary point. As a result, the classical stability theory was created. In the next three decades of the century the exploration of attractors consisting of stationary sets and limit cycles led to the creation of classical theory of oscillations. In the last third of our century the homoclinic and heteroclinic orbits as well as the strange attractors have been intensively investigated.

On the other hand in the fifties and the sixties of our century the frequency-domain methods of investigation of nonlinear systems were set up. At first they were applied and developed only within the frames of absolute stability theory for investigation of global stability of the stationary point. The development of frequency-domain methods was essentially stimulated by the property of invariance of the transfer function and frequency response with respect to linear transformations of the phase space. It should be emphasized in this connection that the form of description of dynamical system by means of transfer function, without participation of coordinates, is usual to engineers and is widely applied in engineering practice.

In the seventies and the eighties it became clear that the tool of frequency-domain methods can be applied successfully for the investigation of stability of stationary sets, for solution of problems of existence of cycles and homoclinical orbits as well as for the estimation of dimension of attractors. And this book is devoted to the consecutive exposition of this point of view.

The fundamentals of frequency-domain methods and of absolute stability theory are given in the two chapters of the first part. We tried to make our exposition as simple as possible here in order that every postgraduate familiar with the standard university courses of linear algebra, mathematical analysis and differential equations could master the fundamentals of frequency-domain methods. We tried to expound frequency-domain methods in spirit of excellent books by M. A. Aizerman and F. R. Gantmakher and by S. Levshetz. We took into account of course new results, contemporary trends and our own educational experience.

There exist two different methods in the generating of stability results in frequency-domain form. They are the application of Yakubovich-Kalman lemma about solvability of matrix inequalities and the constructing of Popov functional.

The Yakubovich-Kalman theorem can be regarded as a generalization for the nonlinear case of a famous theorem about the existence of Lyapunov function of the type of the quadratic form for a linear system with constant coefficients. That is why the Yakubovich-Kalman theorem is often used in the framework of direct Lyapunov method.

The Popov functional is the scalar product in the L2-space of two functions depending on solutions of the dynamical system. The elements of L2-space are transferred by means of the unitary operator (the Fourier transform) into more convenient for investigation space of images L2 where the frequency response appears in a natural way. With the help of the latter the estimates of the scalar product in L2 are brought about. Since the transform is unitary the same estimates are preserved in the space L2. The estimates give the opportunity to make various conclusions about stability and other qualitative properties of the system.

It is interesting to note that in spite of the difference of the tool of the investigation the both methods often give the same results. On the other hand for certain problems the success can be achieved only by one of them. Thus, the frequency-domain conditions of the existence of cycles and homoclinic orbits have been obtained by now only by means of Yakubovich-Kalman theorem, and the stability conditions of the synchronization system with delay have been established with the help of Popov functionals.

Proceeding from this, each of the first three parts of the book, which are devoted to stability of the unique equilibrium, to stability of stationary sets and to the problem of existence of cycles, contains two chapters. One of them demonstrates the application of Yakubovich-Kalman theorem and the other is based on the Popov method.

In the second part the problem of stability of stationary sets of a class of smooth dynamical systems is considered. By such class of dynamical systems many important classes of electric and electronic systems, such as Chua's circuits and systems of phase synchronization (phase-locked loops) are described. The latter have the cylindrical phase space. For these systems, in the book a special method of constructing of Lyapunov functions and Popov functionals is presented, the latter containing solutions of certain comparison systems. We shall note that continual stationary sets appear also in discontinuous relay systems and the systems with solid (Coulomb) friction. Frequency-domain investigation of these systems is expounded in the monograph [Gelig et al. 1978] where the theory of differential inclusions is systematically set forth. The limited capacity of this book made us confine ourselves only to smooth dynamical systems.

In the third part of this book the problem of the existence of cycles and of the estimation of their frequency is considered. The powerful tool of investigation of cycles is the Poincare mapping. If one succeeds to prove that the Poincare mapping transfers the transversal cross-section, on which it is defined, into itself, then by a certain theorem about a fixed point one can deduce the existence of a cycle. That is why the problem of existence of a cycle often can be reduced to the estimation of the Poincare mapping. In the third part of the book various frequency-domain estimates of the Poincare mapping are presented. For the systems with the cylindrical phase space two kinds of the cycles are possible: the cycles of the first kind remain closed in the covering space, the cycles of the second kind lose the closure property there. Both for the cycles of the first kind and for the cycles of the second kind frequency-domain criteria of existence are obtained.

Analogous tool is used in the forth part in order to establish the frequency-domain criterion of existence of homoclinic orbits. For the systems with the cylindrical phase space. Such orbits appear when one transfers in the parameters space of the system from the region of gradient-like behavior to the region of existence of circular solutions and cycles of the second kind. We present in this book a frequency-domain criterion of the existence of a homoclinic orbit which can be regarded as a generalization of well-known Tricomi theorem about the existence of a separatrix loop.

In the fifth part the short review of basic notions of the dimension theory is brought about. Principal attention is paid here to the Hausdorff dimension which is one of the basic characteristics of strange attractors. We present analytical methods of obtaining of upper estimates of Hausdorff measure and dimension of attractors. Then frequency-domain estimates of Hausdorff dimension of attractors are demonstrated. These results are applied to the well-known Lorenz system.

Contents

I    Stability of Control Systems with the Unique Equilib-
rium	1

1	Classical Theory of Absolute Stability	3

1.1	Feedback Control Equation and its Transfer Function		3

1.2	Controllability. Observability. Kalman Duality Principle		4

1.3	The Transfer Function of Controllable and Observable Linear Block  .	12

1.4	Stable Linear Blocks		14

1.4.1    Hermite-Michailov Criterion		17

1.5	Stabilizability of Linear Block		18

1.6	Stability of Linear Feedback System. Nyquist Criterion	. .	20

1.7	Lyapunov Stability. Direct Lyapunov Method   . . . .		22

1.8	Absolute Stability of Control Systems		28

1.9	The Employment of Lyapunov Functions for Investigation of Absolute
Stability		30

1.10 Yakubovich-Kalman Frequency-Domain Theorem		32

1.11 Theorem about Strict Frequency-Domain Inequality		41

1.12 Lyapunov Matrix Inequalities. Necessary and Sufficient Conditions of
Solvability		43

1.13 Circle Criterion		46

1.14 Popov Criterion		48

1.14.1   Geometrical Interpretation of Popov Criterion		51

1.15	Aizerman Conjecture. Kalman Conjecture		54

2	Absolute Stability of Control Systems Described by Integral Volterra
Equations	59

1.16 Alternative Mathematical Description of Feedback Control System 	59

1.17 A Priori Integral Estimates Method. General Stability Theorem..	61

1.18 The Case of Stationary Nonlinear Function. Popov Criterion		81

1.19 The Case of Differentiable Nonlinearity		96

1.20 Critical Cases		101

1.20.1 The Case of a Couple of Pure Imaginary Poles		101

    - The Case of a Zero Pole and a Couple of Pure Imaginary

Poles                                                                              107

1.20.3 The Case of Two Zero Poles		107

1.20.4 The Case of One Zero Pole	 108

II    Asymptotic Behavior of Systems with Multiple Equi-
libria	111

3	Control Systems Described with Ordinary Differential Equations 113
A  Basic Definitions. Dichotomy. Systems with Finite Equilibria 113

- Global Asymptotic Properties of Differential System		113

- Frequency-Domain Criterion of Dichotomy		118

- Global Behavior of Chua's Circuits		125

B    Systems with Denumerable Equilibria	133

2.4	Pendulum-Like Feedback Systems		133

- Dichotomy of Pendulum-Like Systems. Gradient-Like Behavior of Pen
dulum-Like Systems with Nonlinearities Having Zero Mean-Value   . .	141

- Extension of the Circle Criterion. Invariant Cones		143

- Extension of the Method of Invariant Cones		157

- Systems with One Nonlinearity and a Bounded Forcing Term .	157

- Systems with Vector-Valued Nonlinearities		159

- Bakaev Stability		161

- The Method of Periodic Lyapunov Functions. The Bakaev-Guzh Tech
nique		165

- The Bakaev-Guzh Technique in the Case of Differentiable Nonlinearities 169

C    Non-Local Reduction Method	177

- Lyapunov-Type Stability Theorems		178

- Second-Order Pendulum-Like Equations    		185

- Application of Non-Local Reduction Idea to Pendulum-Like Systems .	201

- Stability Investigation of Phase-Locked Loops by Non-Local Reduction
Method		208

- Non-Local Reduction Method for Non-Autonomous Pendulum-Like
Systems		214

- Non-Local Reduction of Higher Dimensional Systems to Autonomous
Systems of the Second Order		224

- Localization of Attractors		241

- Sharpening of Circle Criterion by Means of Non-Local Reduction Method 249

4	Systems Described by Volterra Integro-Differential Equations	    259

- Volterra   Integro-Differential   Equations   with   Periodic   Nonlinear
Functions. General Properties of Solutions		259

- Preliminary Results of the Method of A Priori Integral Estimates for
Integro-Differential Equations		264

- Bakaev-Guzh Technique		272

- Non-local Reduction Method .	   278

2.23 Sharpening of Circle Criterion for Integro-Differential Equations   . .    292

III    Circular Solutions and Cycles	307

5   Existence of Circular Solutions and Cycles for Systems Described
with Ordinary Differential Equations	309

- Periodic Solutions of a Control System with a Nonlinearity from the
Hurwitzian Sector	    309

- Periodic Solutions of Dissipative Systems	    332

- Pendulum-Like Systems with a Single Sign-Constant Nonlinearity  346

- Existence of Circular Solutions and Cycles of the Second Kind of
Pendulum-Like Systems    	    348

- Circular Solutions and Cycles of the Second Kind in Concrete Systems 358

- Estimation of the Period of a Cycle of the Second Kind	    368

- Cycles of the First Kind in the Pendulum-Like Systems	    381

6  Necessary Conditions of Gradient-Like Behavior for the Systems
Described by Integro-DifFerential Equations	397

- Frequency-Domain Criterion of Existence of Circular Solutions for an
Integro-Differential Equation with a Periodic Nonlinearity    	    397

- Estimation of the Period of Periodic Solutions of the Second Kind  404

IV	Existence of Homoclinic Orbits	415

7  Homoclinic Orbits in Pendulum-Like Systems	417

- Homoclinic Orbits. Preliminary Consideration		417

- Homoclinic Orbits of Pendulum-Like Systems with One Nonlinearity 	420

- Dynamics of Synchronous Machines		430

V	Dimension of Attractors	437

8  Frequency-Domain Estimates of Hausdorff Dimension of Attractors 439

- Preliminary Considerations		439

- Topological Dimension		442

5.3   Hausdorff Measure and Hausdorff Dimension		445

- Differentiable Mappings: Upper Estimates of Hausdorff Dimension of
Compacts		453

- Differential Equations:   Upper Estimates of Hausdorff Dimension of
Attractors		457

- Frequency-domain Estimates of Hausdorff Dimension of Attractors.	466

Bibliography	477

Index		497